| COMPANY/ PROJECT NAME or ID/ LOCATION ( City, State) | DATE 4/13/2012 | NEW REVISED | PAGE 1 of 2 |
| --- | --- | --- | --- |
| WORK ACTIVITY (Description): EXCAVATIONS |
| DEVELOPMENT TEAM | POSITION / TITLE | REVIEWED BY: | POSITION / TITLE |
| Aron Yakima | Project Manager | Sean Erlenbeck | Director of Safety |
| Sean Erlenbeck | Director of Safety |  |  |
| MINIMUM REQUIRED PERSONAL PROTECTIVE EQUIPMENT ( SEE CRITICAL ACTIONS FOR TASK-SPECIFIC REQUIREMENTS) |
| REFLECTIVE VEST HARD HAT LIFELINE / HARNESS SAFETY GLASSES | GOGGLES FACE SHIELD HEARING PROTECTION SAFETY SHOES | AIR PURIFYING RESPIRATOR SUPPLIED RESPIRATOR PPE CLOTHING | GLOVES Cut-resistant OTHER Chaps |
| ¹JOB STEPS | ²POTENTIAL HAZARDS | ³CRITICAL ACTIONS TO MITIGATE HAZARDS |
| Setup job site for excavation | Slips, trips and falls | Identify/mark slip, trip and fall hazards. |
|  | Eye and skin contact with Fuel | Wear appropriate PPE if fueling equipment, read MSDS. |
|  | Spills Loose/worn parts Equipment malfunction or damage Site specific hazards | Make sure equipement is not leaking. Fuel equipment at secure location with underlying pavement. Ensure that connections are tight. Replace defective or worn parts. Locate all kill switches Operators to perform daily equipment inspections. If any defects notify equipment manager for repair. Create a TSTI and Excavation Permit for work to be performed |
| Excavate | Underground Interferences Struck by/Crushed by Cave-in protection Safe access and egress Hazardous Atmospheres | Identify all utilities with a RYCOM in area to be Excavated. Mark with a visible indicator that can be easily seen by employees in the work zone. Complete Brieser Excavation Permit Barricade swing radius of excavator Sloping, benching or shoring as required by excavation permit Competent person to verify daily integrity of excavation per excavation permit Install ladders per policy. Inspect before use or install ramps per excavation policy Use of a calibrated 4-gas monitor as needed per excavation permit. |
| Secure Area | Slips,Trips and Falls | Install jersey barricades to protect open excavation from other non-authorized personel. |
| Clean up | Slips, trips and falls | Inspect work area, move material that may cause trips prior to performing work. |
|  | Sprains & Strains | Use proper lifting techniques/team lift. |
| Secure tools. | Slips, trips and falls | Inspect work/staging area. |
|  | Security | Lock equipment. Lock away tools. |

¹