Mast

Safe Work Procedure

| Division: |  | Analysis By: |  | Date: |  |
| --- | --- | --- | --- | --- | --- |
| Department: |  | Supervisor: |  | Frequency: |  |
| Job Title: |  | Approved By: |  | JSA Number: |  |
| Job Title: | 97 Glass removal and replacement | Job Performed By: |  |  |  |

Required Personal Protective Equipment:  Safety glasses, gloves

GENERAL NOTES:  Special tool- suction cup

Job Safety Analysis:

| Step | Description | Hazard | Controls |
| --- | --- | --- | --- |

| 1 | Inspect immediate area to identify hazards before starting the job | Collapse--Contact--Eye----Equipment Damage--Falling Object--Hand | Eliminate unsafe conditions before starting job--Enclose broken glass with cardboard and if completely broken, remove and replace with plywood until new glass is ready to put in place--Entry procedures for windows broken above walkways require barricades and warning tape. |
| --- | --- | --- | --- |

| 2 | Remove old glass | Back Injury--Collapse--Cut--Eye----Falling Object | Dispose of glass in appropriate containers--Match the employee to the task--Personal protective equipment (PPE) should include the following; gloves and safety glasses--Replace broken glass with cardboard or plywood |
| --- | --- | --- | --- |

| 3 | Lift new glass into place | Cut--Falling Object--Muscle Strain | Anchor glass firmly into place--Buddy system for lifting units larger than 3' by 3' square--Lifting techniques--Match the employee to the task--Material handling equipment should include the following; suction cup for larger units--Proper operating procedure should be followed for use of power tools, portable ladders and scaffolds. |
| --- | --- | --- | --- |

| 4 | Inspect immediate area for any fragments of glass | Cut--Puncture | Good housekeeping practice(s) should include the following; clean immediate area and dispose of refuse in a proper container |
| --- | --- | --- | --- |

AUTHORIZED EMPLOYEE INFORMATION:

| ID NUMBER: | LAST NAME: | FIRST NAME: | REMARKS: |
| --- | --- | --- | --- |

JOB HISTORY INFORMATION:

| DATE: | REMARKS: |
| --- | --- |

Approval Signature:										Date: